driftNode

Normal Operation:

-Connect power to Pi
-After GPS signal (indicated by green led) is acquired ROS will startup (takes about 10	minutes)
-Camera node starts last. When led on camera illuminates ROS will start bagging

Restarting Node:

-First verify that all nodes as well as ros core are stopped by entering the following into	the command line: ps -ef | grep ROS and kill any running ROS processes
-Run the startup script: /etc/init.d/driftNodeStartupROS.sh
-The node should now follow normal operation

Starting ROS Manually:

-in a terminal enter roscore
-start the gps node by entering rosrun gps_node_py gps_talker.py in a new terminal
Do not start other nodes until GPS gets signal and updates system time.
-start the imu node by entering rosrun imu_node imu_talker.py in a new terminal
-start the wifi node by entering rosrun wifi_node wifi_talker.py in a new terminal
-start the camera node by entering
rosrun raspicam raspicam_node _width:=1200 _height:=900 _framerate:=2	_quality:=75 _tf_prefix:=pi- & in a new terminal. Don't go below 2 fps, or too	high of a resolution/quality as this will crash the node.
-wait for camera node to start and then enter rosservice call /camera/start_capture
in a new terminal. Once the camera starts capturing, the red led on it will I	lluminate.
-bag the topics by entering rosbag record -a -q --split –size=500000 in a new terminal.
Before recording, be sure to change to directory where you want bag files to go.

Manually Starting ad-hoc Network:

-first make sure the pi is not connected to any networks. If it is delete those networks	from the pi by editing the file (as root) /etc/wpa_supplicant/wpa_supplicant.conf
and delete lines containing information about wireless networks.
-set up network by entering the following:
sudo ifconfig wlan0 down
sudo ifconfig wlan0 up
sudo iwconfig wlan0 mode ad-hoc
sudo iwconfig wlan0 essid "NODE NAME”
sudo ifconfig wlan0 192.168.1.1 netmask 255.255.255.0

Important Files:

-There are some important files in the file system of the Pi that must not be moved or	deleted due to dependencies. These include:
On the desktop: GPSstart.py and GPIOLED.py
In the downloads folder: poco folder and bullet folder